1) Write an assembly	language program to	add up	the numbers from 1 to 20 (inclusive)	and output the result to Port B
init:
.def	counter=r16
.def	bound=r17
.def	sum=r18
main:
ldi	counter,1
ldi	bound,21
clr	sum
loop:
cpc	counter,bound
brge	end
add	sum,counter
inc	counter
rjmp	loop
end:
out PORTB, r18
    ret

2. Write an assembly	language program to	output	the next 10 numbers in memory to Port B. Begin at data space 0x0100 (use register z to	retrieve the numbers)
 init:
.def	counter=r16
.def	bound=r17
main:
ldi	bound, 1
ldi	zh, 0x01
ldi	zl, 0x00
ld	r22, z+
ld	r23, z
cpc	r22, r23
brlo	first
out	PORTB, r22
rjmp	end
first:
out	PORTB, r23
end:
ret

3) Write an assembly	language program to	take the next two numbers in memory starting at data space 0x0100. Compare them and output the greater number (if the numbers are equal,	output	that number). Use register z	to retrieve the	numbers.
:)

4) Write an assembly	language program to	add any 5 binary numbers. Get the numbers	from	the Data Space starts from 0x0100. Output the lower byte of the result to Port B and	the high byte of the result to Port C. (use	register z to get number).

init:
.def	counter=r16
.def	bound=r17
.def	suml=r18
.def	sumh=r19
main:
ldi	bound, 5
ldi	zh, 0x01
ldi	zl, 0x00
ldi	suml, 0
ldi	sumh, 0
ldi	r23, 0
loop:
cpc	zl, bound
brge	end
ld	r22, z+
add	suml, r22
adc	sumh, r23
rjmp	loop
end:
out	PORTB, suml
out	PORTC, sumh
    ret

5) Write an assembly	language program to find the	largest	number in 20 binary numbers read from Data Space. Get the numbers	from the Data	Space	starts from 0x0100. Output the result to Port	B. (use register z to get number)
init:
.def	counter=r16
.def	bound=r17
.def	largest=r18
main:
ldi	bound, 19
ldi	zh, 0x01
ldi	zl, 0x00
ldi	largest, 0
loop:
cpc	zl, bound
brge	end
ld	r22, z+
cpc	r22,largest
brge	largefound
rjmp	loop
largefound:
mov	largest, r22
rjmp	loop
end:
out PORTB, largest
    ret

6) Write an assembly	language program to do the following: get the number N from Data Space at 0x0100, add all numbers in [1, N], Output the lower byte of the result to Port B	and the high byte of the result to Port C. (use register z to	get number) (For example: if	N is 5,	do the	adding	1+2+3+4+5)
init:
.def	counter=r16
.def	bound=r17
.def	suml=r18
.def	sumh=r19
main:
ldi	counter, 1
ldi	zh, 0x01
ldi	zl, 0x00
ldi	r20, 0
ld	bound, z
inc	bound
clr	suml
clr	sumh
loop:
cpc	counter, bound
brge	end
add	suml, counter
adc	sumh, r20
inc	counter
rjmp	loop
end:
out	PORTB, suml
out	PORTC, sumh
  ret